Site Planning Study Guide:

(225 Minutes/3.75 hours)

General Comments:

- Creativity and beauty are not scored on this exam.

- Time is a critical factor – don’t strive for perfection.

- Reasons for failure:

- Miss program elements or don’t’ follow instructions

- Fail to solve problem

- Don’t finish

- Don’t try to improve program

Section 1:

Site Design Vignette – (90 Minutes/1 Hour 30 minutes): (Only Problem)

- Review Program and take notes – 10 minutes

- Turn on grid

- Draw restrictions/setbacks

- Loosely place buildings and scale blocks of elements

- Calculate parking 1, 2 or 3 rows

- Block it out

- Assume all regular size

- Sketch in roads

- Design

- Draw

- Check – 15 minutes

- Ensure program items are not missed!

- Trees:

  - Shade = Use deciduous trees

  - Wind = Use conifers

- Keep trucks away from residential

- Parking:

  - 5/8/8/9’

  - Flow through = allows cars to continuous move past all spaces without leaving the site or backing up.

  - Consider backup safety

  - Passenger side drop offs.

Calculating Parking:

Rough Width	= Total width of all stalls / # of rows (you decide – 2, 3, or 4 typical)

of Rows

= ((#HC stalls x stall width)+ (# of regular stalls x stall width)) / # of rows

eg)	= ((3 x 12’) + (30 x 9’) / 4

= 306/4 = 76.5’

Therefore, 76.5/9’ = approx 8 stalls per row.  Add 29’ x 2 to each end to get approximate rectangle size (so 77’ + 29 + 29 = 135’ (actually works out to 132’ but 135 will give you a sense if it fits ).

Drive Through Parking Configurations: (24’ drive lanes, 9’ x 18’ reg stalls, 12’ x 18’ HC stalls)

|  | Rough Rectangle: 157x107’ – 3 row 157x125’ – 4 row Stall Yield: 3 row = 33-36 4 row = 48-49 |
| --- | --- |
|  | Rough Rectangle: 198x107’ – 3 row 198x125’ – 4 row 198’ wide by (162’ + 36‘ for 2 end rows) Stall Yield: 3 row = 47-50 4 row = 62-63 |
|  | Rough Rectangle: 132x107’ – 3 row 132x125’ – 4 row Stall Yield: 3 row = 24-27 4 row = 33-36 |
|  | Rough Rectangle: 168x107’ – 3 row 168x125’ – 4 row 168’ wide by (132’ + 36‘ for 2 end rows) Stall Yield: 3 row = 38-41 4 row = 47-50 Not as efficient as longer rows (2nd diagram) |

Parking Widths (18’ rows with 24’ drives)

15 MINUTE MANDATORY BREAK

Section 2:

Site Zoning – (60 Minutes/1 Hours): (1st Problem)

- Turn on Grid

- Separate and copy plan and section information

- Plan: - ?? minutes

- Zoom in and mark our site improvement areas with sketch lines

- Use circles along curvy areas

- Draw secondary construction area

- Sketch out setbacks or other restrictions

- Sketch out buildable area

- Sections:

- Zoom in and track down sketch lines for contours

- Draw Grade Line!!!!

- Erase sketch lines

- Zoom in and track set backs down

- Sketch height restrictions

  - Trick don’t miss this (i.e. Any portion of bldg below 160’ elev shall maintain a 20’ setback from property line = notches bottom flors, but shows as buildable area in plan.

- Draw in buildable area.

Definitions:

Site Improvements = Areas where surface improvements are allowed

Building Construction = Area where buildings are allowed.

Easements = Site improvements typically allowed in easements unless noted otherwise.

Site Grading Vignette – (30 Minutes/1/2 Hour): (2nd Problem)

- Figure out which scenario applies (see below i.e flat/sloped pad).

- Draw rough sketch lines for path of water.

- Adjust contours accordingly.

- Use circles to check slope but make sure interval is correct i.e.) ½’, 1’, 2’, 5’

Eg,  20% = 20/100    Therefore 1/5

Scenarios:

1.  Flat Pad:

Bring next lowest elevation around and create swales on both sides – Regrade all around.

- Use circles to check distances

- Look at contour intervals 1, 2, or 5’ typ.

- Don’t forget to check ½ slope between pad and 1st contour line.

2.  Sloped Pad:

Create gulleys around.

Double V at top above pad.

3.  Road:

Usually crown in middles with gulleys at sides.

Even intervals to contours (spacing).

Slope and Checking:

1 foot contour intervals:

25% slope 25/100=1/x     Therefore x=4

  - Therefore draw a circle with 4’ radius to check.

20% slope 20/100=1/x     Therefore x=5

- Therefore draw a circle with 5’ radius to check.

1/2 foot contour intervals:

20% slope 20/100=0.5/x     Therefore x=2.5’

- Therefore draw a circle with 2’ 6” radius to check.

Definitions:

Swale = Ditch

Berm/Crown = Bump